## Slide 2: Drywall
Does it BURN?

## Slide 3: Problem
Is fire retardant drywall more effective at slowing fires because it has more water content?

## Slide 4: Drywall
Drywall is the common name for gypsum board
  Gypsum compressed between two sheets of cardboard
  Gypsum = calcium sulphate
  Hydrate
  About 20% water

## Slide 5: Fire Resistance
Gypsum doesn’t burn
Will prevent fire from spreading until water has evaporated
  Shrinking will cause cracks in board
  Crumble and allow fire to spread

## Slide 6: Hypothesis
Fire retardant drywall contains a higher percentage of water than standard drywall, it isn’t just the thickness
  Fire retardant drywall is designed to last longer before cracking
  More water would mean more time before a crack occurred

## Slide 7: Materials
Sheet of fire retardant and standard drywall
Heat gun
Temperature probes
Sheet of foam insulation
Metal tape (fire resistant)

## Slide 8: Procedure
Cut 12 pieces of each type of drywall, 30cm x 30cm
Build box out of boards of insulation, large enough to fit piece of drywall but preventing air from getting in/out
Connect probe to each side of drywall square (use tape) and in hole in box
Place drywall in front of box

## Slide 11: Continued
Fire heat gun from a distance of 30cm for 120 seconds, continue recording for another 120 seconds to cool
Allow gun to cool and probes to balance
Remove probes from drywall, and proceed with next sample
Use 4 standard and 4 fire retardant samples

## Slide 13: Continued (Again)
Baked 4 of each type to find mass loss and determine bake time
Baked a fresh batch of 4 of each type
Repeated heat transfer tests using these samples
Record all data

## Slide 14: Removing the Water
Baking removes water (evaporation)
  Used 4 samples of each type to decide time and temp to be used
Baked in oven for an hour at 175°C
  Chose this temperature because it was low enough that the cardboard wouldn’t burn
  Chose this time because it started burning anyways if over an hour

## Slide 15: Logger Pro

## Slide 16
Experimental Variable
  Type of Drywall
Experimental Groups
  Fire-Retardant and Standard Gypsum Board
Control Group
  No heat gun applied

## Slide 17: Control Variables
Same Equipment
  Heat gun
  Temperature probes
  Oven
Drywall brand
  Stored in same surroundings
  Cut and tested at same time

## Slide 18: Initial Heat Transfer
Box might not be air tight, inconsistencies
  No conclusions
  Air temperature rose at unusual rates
Probe malfunction for fire retardant
  No air temperature data
Chart: Standard
| 0 | 120 | 240
Rear | 21.1247 | 26.8479 | 30.3659
Air | 19.0938 | 29.9128 | 28.2642
Chart: Fire Retardant
| 0 | 120 | 240
Rear | 22.7252 | 31.4338 | 31.7649

## Slide 19: Water Loss
Chart: % Mass Lost
| 0 | 20 | 40 | 60
fireproof | 0 | 0.0019875 | 0.036889 | 0.081357
standard | 0 | 0.010185 | 0.054111 | 0.11611

## Slide 20: Baked Heat Transfer
Made better seal
  Deviation not even visible on chart
  Decreased deviation makes data useful
Significantly different from first run
Chart: Standard Drywall (Baked)
| 0 | 120 | 240
Rear | 24.7568 | 26.1926 | 30.2973
Air | 22.1405 | 24.0843 | 25.1256
Chart: Fire Retardant (Baked)
| 0 | 120 | 240
Rear | 24.0336 | 24.4035 | 26.5221
Air | 23.6384 | 24.5516 | 25.2325

## Slide 21: Max Surface Heat
Chart: 
| 0 | 120 | 240
standard | 19.9208 | 114.8142 | 62.1676
fire ret. | 22.3704 | 96.4741 | 50.038
baked st | 24.895 | 114.087 | 69.9175
baked fire | 24.1899 | 101.6044 | 66.135

## Slide 22: Conclusion
Fire retardant drywall actually contains less water, but conducts less heats
Surface temperature is lower, but so is rear temperature
  Heat might be reflected off, or fire retardant drywall has some other quality I overlooked

## Slide 23: Further Research
Fire retardant drywall has additional chemicals that cause it to expand, meaning less calcium sulphate
Fiber glass strands weaved through it will also mean less gypsum and water storage capabilities
Drywall, especially standard, will have defects and errors

## Slide 24: What to Change
Find a better way to create an airtight box
Reduce the number of variables
  Quality of drywall
Get better testing equipment

## Slide 25: Further Testing
Find out where the heat goes
Find ideal combination of chemicals
Find differences between other brands of drywall
Be able to use realistic fire temperatures

## Slide 26
 | Average Temp. |  |  |  |  | St. Deviation |  | 
Time | Surface | Rear | Air |  | Time | Surface | Rear | Air
0 | 24.19 | 24.03 | 23.64 |  | 0 | 0.62 | 0.42 | 0.45
120 | 101.60 | 24.40 | 24.55 |  | 120 | 4.85 | 0.37 | 0.39
240 | 66.13 | 26.52 | 25.23 |  | 240 | 1.98 | 0.40 | 0.35